## Slide 1: AR Assisted Orbital Floor Implant Shaping
Augmented Reality Course Project
Yihao Liu
Mentors: Wenhao Gu , Ehsan Azimi, Dr. Peter Kazanzides

## Slide 2
Background
Orbital floor reconstruction
Fractured eye socket bones
Place an implant
[1] Kazanzides, P. (2020). Navigation for Orbital Floor Fracture Repair. [PowerPoint Slides]

## Slide 3: Motivation and Solution
Orbital floor reconstruction
  Fractured eye socket bones
  Need: correct shape of the implant
    Takes time and trials in surgery
Completed solution:
  Manually move the implant to skull
  Digitize implant and calculate heat map to show discrepancy
  Display corresponding eye socket area
  Display a highlighted area using mesh

## Slide 4: Solution
Implant Surface Digitalization
  Option1: Inside-out, HoloLens
    Tracked pointer: AR checkerboard marker
  Option2: Outside-in, Polaris
    Tracked pointer: Passive reflective ball markers
    Transformation between Polaris and Unity
      attached marker frame
Heat map calculation
  Closest point algorithm
  Octree data structure
Polaris image and product info: https://www.ndigital.com/medical/products/
Hololens image and product info: https://docs.microsoft.com/en-us/hololens/hololens1-hardware

## Slide 5: Transformation Map

## Slide 6: System Diagram
1.
2.
3.
4. & 5.
UDP

## Slide 7: Heat Map – Mesh
Model mesh
  Vertices
  Triangle indices
.ply polygon file
Simple concept demo:
  - Three triangles
  - Colored vertices

## Slide 8: Closest Point Algorithm
Bounding Spheres
  Triangle center
Octree
Images from Computer-integrated Surgery I JHU, Russ H. Taylor

## Slide 9: Demo

## Slide 10: Challenges and Future Works
Unity handedness
  Convert to left handedness first, then do transformation
Data handling
  .ply file read and write
  Mesh data transmission (full buffer)
Procedure time
  3 minutes excluding pivot calibration (searching algorithm takes longest)
Automated procedure
  Substitute keyboard input (possibly voice control)

## Slide 11: Mesh - Other Application
Model high-lighting
Educational use
Multi-user interaction
CT image visualization

## Slide 12: Work in other projects
Closest point algorithm – Yihao Liu, Tim Bernard, Programming Assignment 4 CIS I
Polaris interface – Yihao Liu, Nikhil Dave, AR assisted craniofacial surgery, CIS II project
Reading List
Hussain, R., Lalande, A., Guigou, C., and Bozorg Grayeli, A. (2019). Contribution of Augmented Reality to Minimally Invasive Computer-Assisted Cranial Base Surgery, IEEE Journal of Biomedical and Health Informatics.
Gsaxner C., Pepe, A., Wallner, J., Schmalstieg, D., and Egger, J. (2019). Markerless Image-to-Face Registration for Untethered Augmented Reality in Head and Neck Surgery, MICCAI 2019.
Li, Y., Chen, X., Wang, N., Zhang, W., Li, D., Zhang, L., Qu, X., Cheng, W., Xu, Y., Chen, W., and Yang, Q. (2018). A wearable mixed-reality holographic computer for guiding external ventricular drain insertion at the bedside, Journal of Neurosurgery JNS, 131(5), 1599-1606.
Thank you